## Slide 1: GRRF-85 main approved contents
Contains confidential proprietary and trade secrets information of CNH Industrial. Any use of this work without express written consent is strictly prohibited.
Turin, Italy
January 2018
Claudio Prina
IVECO EHSA – Hydraulics&Pneumatics

## Slide 2: GRRF-85 (Geneva, December 11th 2017)
Main items reviewed during the last session:
-) ACSF (Automatically Commanded Steering Function) Cat. C requirements and tests;
-) ESF (Emergency Steering Function) requirements and tests;
-) Special requirements to be applied to the safety aspects of electronic control systems (Annex 6)
-) Transitional provisions for series 02 (ASCF cat. A and B1) and 03 (ACSF cat. C, ESF, Annex 6 – CEL) of amendments to reg. 79
The text will be submitted to WP.29 (World Forum for Harmonization of Vehicle Regulations) March 2018 session.
Revision of UN-ECE Reg. 79 - Steering

## Slide 3: Backup
ACSF Cat. C

## Slide 4
Automatically commanded steering function (ACSF)
 | "Automatically commanded steering function (ACSF)" means the function within an electronic control system where actuation of the steering system can result from automatic evaluation of signals initiated on-board the vehicle, possibly in conjunction with passive infrastructure features, to generate control action in order to assist the driver |  |  |  |  | 
 | ACSF assists the driver who carries out the manoeuvre |  | ACSF is initiated/activated by the driver and ACSF performs the manoeuvre |  |  | 
Categories (ECE-UN Reg. 79) | A | B1 | B2 | C | D | E
Outline of classification | a function that operates at a speed no greater than 10 km/h to assist the driver, on demand, in low speed or parking manoeuvering. It includes remote parking control (RPC). | a function which assists the driver in keeping the vehicle within the chosen lane, by influencing the lateral movement of the vehicle. Hands-on | a function which is initiated/activated by the driver and which keeps the vehicle within its lane by influencing the lateral movement of the vehicle for extended periods without further driver command or confirmation Hands-off | a function which is initiated/activated by the driver and which can perform a single lateral manoeuvre (e.g. lane change) when commanded by the driver | a function which is initiated/activated by the driver and which can indicate the possibility of a single lateral manoeuvre (e.g. lane change) but performs that function only following a confirmation by the driver | a function which is initiated/activated by the driver and which can continuously determine the possibility of a manoeuvre (e.g. lane change) and complete these manoeuvers for extended periods without further driver command/confirmation
Type of manoeuvre | Parking | Lane keeping | Lane keeping | Single lateral manoeuvre (lane change) | Single lateral manoeuvre (lane change) | Multiple lateral manoeuvre (lane changes)
Driver/ACSF tasks | Driver commands ACSF operates | Driver operates ACSF assists | ACSF operates; Driver commands/confirms | ACSF operates; Driver commands | ACSF operates; Driver confirms | ACSF operates; Driver initiates the function then no commands or confirmations
SERIES 02
SERIES 03
TBR
TBR

## Slide 5: ACSF Cat. C
Lane change procedure
A lane change procedure in the case of ACSF Cat. C starts when the direction indicator lamps are activated by a deliberate action of the driver and ends when the direction indicator lamps are deactivated. It comprises the following operations:
-) activation of the direction indicator lamps by a deliberate action of the driver;
-) lateral movement of the vehicle towards the lane boundary;
-) lane change manoeuvre;
-) resumption of the lane keeping function;
-) deactivation of direction indicator lamps.
The lane change manoeuvre is part of the lane change procedure and:
-) starts when the outside edge of the tyre thread of the vehicle’s front wheel closest to the lane markings touches the inside edge of the lane marking to which the vehicle is being manoeuvred;
-) ends when the rear wheels of the vehicle have fully crossed the lane marking.
Revision of UN-ECE Reg. 79 - Steering

## Slide 6: ACSF Cat. C
ACSF Cat. C is a function which is initiated/activated by the driver and which can perform a single lateral manoeuvre (e.g. lane change) when commanded by the driver
Main general requirements:
-) a vehicle equipped with an ACSF of Cat. C shall also be equipped with an ACSF of Cat. B1 (i.e. lane keeping with hands on); when the ACSF Cat. C is activated (standby) the ACSF of Cat. B1 shall aim to center the vehicle in the lane;
-) the default status of the system shall be off (unless in stop/start systems);
-) the vehicle shall be equipped with a means for the driver to activate (standby) and deactivate (off) the system. The same means as for an ACSF Cat. B1(lane keeping) may be used;
-) the system shall only be activated (standby) after a deliberate action by the driver. Activation shall only be possible on roads where pedestrians and cyclists are prohibited and which are equipped with a physical separation that divides the traffic moving in opposite directions and which have at least two lanes in the direction the vehicles are driving; in case of a transition from a road type permitting ACSF Cat.C to a road type not permitting it, the system shall be deactivated automatically;
-) it shall be possible to deactivate the system (off) at any time by a single action of the driver, and further to this action, the system shall only be able to be reactivated (standby) by a deliberate action of the driver;
-) a steering input by the driver shall override the steering action of the system, applying a steering effort not exceeding 50N;
HMI:
-) when the system is in standby mode (i.e ready to intervene), an optical signal shall be provided to the driver;
-) when the lane change procedure is ongoing an optical signal shall be provided to the driver;
-) when the lane change procedure is suppressed , the system shall clearly inform the driver by an optical warning signal and additionally by an acoustic or haptic warning signal;
-) a system failure shall be signalled immediately to the driver by an optical warning signal; if a system failure occurs during a lane change manoeuvre, the failure shall be signalled to the driver by an optical, and an acoustic or haptic warning;
-) the system shall provide a means of detecting that the driver is holding the steering control: if , after a period no longer than 3 s after the initiation of the lane change procedure, the driver is not holding the steering control, an optical warning signal shall be provided. The warning signal shall be active until the driver is holding the steering control or until the system is deactivated;;
-) all these HMI optical signals shall be easily distinguishable from each other.
Revision of UN-ECE Reg. 79 - Steering

## Slide 7: ACSF Cat. C
Lane change procedure
-) the initiation of a lane change procedure of ACSF Cat. C shall only be possible if an ACSF Cat. B1 (lane keeping) is already active;
-) the lane change procedure requires and shall start immediately after a manual activation by the driver of the direction indicator to the intended side for the lane change;
-) the lateral movement shall not start earlier than 1 s after the start of the lane change procedure and shall be completed as a continuous movement;
-) the lane change manoeuvre shall be completed in less than:
-) 5 s (M1, N1)
-) 10 s (M2, N2, M3, N3);
-) once the lane change manoeuvre has been completed, ACSF Cat. B1 lane keeping function shall resume automatically;
-) the direction indicator shall remain active throughout the whole period of the lane change manoeuvre and shall be deactivated by the system no later than 0.5 s after the resumption of ACSF Cat. B1 lane keeping;
-) a critical situation is deemed to be critical when, at the time of the lane change manoeuvre starts, an approaching vehicle in the target lane would have to decelerate at a higher level than 3 m/s2, 0.4 seconds after the lane change manoeuvre has started, to ensure the distance between the two vehicles is never less than that which the lane change vehicles travels in 1 second;
-) the lane change procedure shall be suppressed automatically by the system when:
a) the system detects a critical situation;
b) the system is overriden or switched off by the driver;
c) the system reaches its boundaries (e.g. lane markings are no longer detected);
d) the system has detected that the driver is not holding the steering control at the start of the lane change manoeuvre;
e) the direction lamps are manually deactivated by the driver;
f) the lane change manoeuvre has not commenced within 5 s after the manual activation by the driver of the direction indicators;;
g) the lateral movement is not continuous;
-) the ACSF Cat. C shall be able to detect vehicles approaching from the rear in an adjacent lane up to a distance Srear declared by the vehicle manufacturer and shall not be less than 55 m; the test shall be conducted using a two-wheeled motor vehicle of Cat. L3 as approaching vehicle;
-) the ACSF Cat. C shall be able to detect the blindness of the sensor (e.g. due to dirt, ice, snow) and , upon detection of blindness, prevented from performing the lane change manoeuvre.
Revision of UN-ECE Reg. 79 - Steering

## Slide 8: ACSF Cat. C
Revision of UN-ECE Reg. 79 – Steering- Lane change procedure

## Slide 9: ACSF Cat. C
System information data
Beyond what prescribed in Annex 6 of Reg. 79, the following data shall be provided to the Technical Service at the time of type approval:
-) the conditions under which the system can be activated and the boundary conditions;
-) information about how the system detects that the driver is holding the steering control;
-) the means to override and to suppress or cancel;
-) information about how the failure warning signal status and the confirmation of the valid software version related ACSF performance can be checked via the use of an electronic communication interface;
-) documentation about which system software version related ACSF perfomance is valid. This documentation shall be updated whenever a software version was amended.
Revision of UN-ECE Reg. 79 - Steering

## Slide 10: ACSF Cat. C
Tests to be performed
If not specified otherwise all vehicle test speeds shall based on 130 km/h. If not specified otherwise, the approaching vehicle shall be a type-approved high volume series production vehicle. The vehicle manufacturer shall demonstrate to the satisfaction of the Technical Service that the requirements are fulfilled for the whole speed range and this may be achieved on the basis of appropriate documentation appended to the test report.
The following tests are prescribed:
-) lane change functional test;
-) minimum activation speed test;
-) overriding test;
-) lane change procedure suppression test;
-) sensor performance test;
-) sensor blindness test;
-) engine start/run cycle test;
Revision of UN-ECE Reg. 79 - Steering

## Slide 11: Backup
ESF

## Slide 12: ESF (Emergency Steering Function)
Emergency steering function (ESF) means a control function which can automatically detect a potential collision and automatically activate the vehicle steering system for a limited duration, to steer the vehicle with the purpose of avoiding or mitigating a collision, with:
-) another vehicle driving* in an adjacent lane:
i) drifting towards the path of the subject vehicle and/or;
ii) into which path the subject vehicle is drifting and/or;
iii) into which lane the driver initates a lane change manoeuvre.
-) an obstacle obstructing the path of the subject vehicle or when the obstruction of the subject vehicle’s path is deemed imminent.
*the vehicle may be driving in the same or the opposite direction as the subject vehicle
Revision of UN-ECE Reg. 79 - Steering

## Slide 13: ESF (Emergency Steering Function)
-) every intervention shall immediately be indicated to the driver by an optical warning signal which is displayed for at least 1 s or as long as the intervention exists, whichever is longer. In the case the intervention is controlled by an electronic stability control (ESC) or a vehicle stability function, the ESC flashing tell-tale indicating the intervention of ESC may be used, as long as the intervention exists, as an alternative to the optical warning signal;
-) any ESF shall only start an intervention in the case where a risk of a collision is detected;
-) any vehicle fitted with ESF shall be equipped with means to monitor the driving environment (e.g. lane markings, road edge, other road users) in line with the specified use case and these means shall monitor the driving environment at any time the ESF is active;
-) an automatic avoidance manoeuvre initiated by an ESF shall not lead the vehicle to leave the road;
-) in the case of an ESF intervention on a road o a lane delimited with lane markings on one or both side(s), an automatic avoidance manoeuvre initiated by an ESF shall not lead the vehicle to cross a lane marking; however, if the intervention starts during a lane change performed by the driver or during an unintentional drift into the adjacent lane, the system may steer the vehicle back into its originale lane of travel;
-) in the absence of a lane marking on one or on both side(s) of the vehicle, a single ESF intervention is permitted, provided that it doesn’t produce a lateral offset of the vehicle greater than 0.75 m in a direction where the lane marking is absent;
-) the ESF intervention shall not lead the vehicle to collide with another road user;;
-) any intervention of an ESF shall be indicated to the driver with an optical and with an acoustic or haptic warning signal to be provided at the latest with start of ESF intervention; for this purpose, appropriate signals used by other warning systems (e.g. blind spot detection, lane departure warning, forward collision warning) are deemed to be sufficient to fulfill the requirements for the respective optical, acoustic or haptic signals above;;
-) a system failure shall be indicated to the driver with an optical warning signal;
-) the steering control effort necessary to override the directional control provided by the system shall not exceed 50 N;
Revision of UN-ECE Reg. 79 - Steering

## Slide 14: ESF (Emergency Steering Function)
System information data
The following data shall be provided, beyond other documentation, to the Technical Service at the time of type approval:
-) use case(s) where ESF is designed to operate;
-) the conditions under which the system is active (e.g. vehicle speed range);
-) how ESF detects a risk of collision;
-) description of the means to detect the driving environment;
-) how to deactivate/activate the function;
-) how it is ensured that the overriding force does not exceed the limit of 50 N.
Revision of UN-ECE Reg. 79 - Steering

## Slide 15: ESF (Emergency Steering Function)
Tests to be performed
The vehicle shall be driven with an activated ESF on a road with lane markings on each side and positioned within those lane markings. The test conditions and the vehicle speeds shall be within the operating range of the system as declared by the manufacturer.
-) unintentional lateral manoeuvre;
-) intentional lateral manoeuvre;
-) object avoidance (with lane markings and without lane markings);
-) false reaction test.
Revision of UN-ECE Reg. 79 - Steering

## Slide 16: Backup
Special requirements to be applied to safety aspects of electronic control systems
Annex 6

## Slide 17: Special requirements of electronic control systems
In Annex 6 special requirements are prescribed for documentation, fault strategy and verification with respect to the safety aspects of Complex Electronic Systems as far as it refers to Reg. 79.
Complex Electronic Vehicle Control Systems are those electronic control systems in which a function controlled by an electronic system or the driver may be over-ridden by a higher level electronic control system/function. A function which is over-ridden becomes part of the complex system, as well as any overriding system/function withing the scope of the UN-ECE Reg.79. The transmission links to and from overriding system/functions outside the scope of this regulations shall also be included.
The Technical Service shall assess the documentation package to show that the system:
Is designed to operate, under non-fault and fault conditions, in such a way that it does not induce safety critical risks;
Respects, under non-fault and fault conditions, all the appropriate performance requirements specified elsewhere in Reg.79;
Was developed according to the development process/method declared by the manufacturer
Documentation shall be made available in two parts:
Formal documentation package (supplied to Technical Service at the time of submission of the type approval application) available at the Approval Authority for at least 10 years counted from the time when production of the vehicle id definitely discontinued;
Additional material, and analysis data, which shall be retained by the manufacturer, but made open for inspection at the time of type approval, and available at the manufacturer for at least 10 years counted from the time when production of the vehicle id definitely discontinued:
i) a description that gives a simple explanation of the control functions and methods to achieve the objectives, including a statement of the mechanism(s) by whiche control is exercised;;
ii) interconnections within the system shall be shown by a circuit diagram for the electric transmission links, by a piping diagram for pneumatic or hydraulic transmission equipment and by a simplified diagrammatic layout for mechanical linkages;
iii) a statement provided by the Manufacturer which affirms that the strategy chosen to achieve the system objectives will not, under non-fault conditions, prejudice the safe operation of the vehicle;
iv) regarding software, the outline architecture, design methods and tools, the means how the realization of the system logic was determined during the design and development process;
v) explanation to the Technical Service of the design provisions built into the system so as to generate safe operation under fault conditions;
vi) analysis data (Hazard/Risk analysis, FMEA/FTA, validation plans and results, HIL, vehicle operational testing)
Revision of UN-ECE Reg. 79 - Steering

## Slide 18: Backup
Transitional provisions

## Slide 19: Transitional provisions Reg. 79 for 02 and 03 series of amendments*
Applicable to the series 02 (ACSF cat. A and B1) of amendments
Series 01 UN-TA acceptance
2018
* To be submitted to March 2018 session of WP29
2019
2020
2021
1st APR
1st APR
1st SEP
1st SEP
Series 01 UN-TA acceptance only if first issued before 1st April 2021
No series 01 UN-TA acceptance
Series 02 UN-TA acceptance
Series 02 UN-TA acceptance only if first issued before 1st September 2019
No series 02 UN-TA acceptance*
Applicable to the series 03 (ACSF cat. C, ESF, Annex 6 – CEL) of amendments
*except for vehicles not affected by provisions introduced with series 03 (ESF, ASCF-C, CEL Annex 6): for them series 02 UN-TA will continue to be accepted